## Slide 1: GEOG 3319: Geographic Field Techniques
Yaqian He, PhD
Assistant Professor
Department of Geography
Lecture 06 Future and Application of GNSS

## Slide 2
GNSS Family
  GPS
  GLONASS
  Galileo
  BeiDou
  QZSS
  IRNSS
    Why GNSS?
    GNSS Application
Overview

## Slide 3
1978
6 Orbital planes
MEO
24 Satellites (currently 31)
55° Inclination Angle
Altitude 20, 200 km
½ sidereal day period
GPS
https://www.e-education.psu.edu/geog862/node/1860
Notes: 1993, 24 satellites
Ascending node
23h56min, solar day is 24 hours

## Slide 4
GPS
https://smallsat.files.wordpress.com/2013/01/issgroundtrack_011.png
GPS Ground Track
  The vertical projection of the satellite's orbit onto the surface of the Earth
Notes: 1993, 24 satellites

## Slide 5
GPS
https://www.gps.gov/systems/gps/space/#:~:text=The%20satellites%20in%20the%20GPS,any%20point%20on%20the%20planet
GPS satellite
https://www.e-education.psu.edu/geog862/node/1860
Notes: 1993, 24 satellites, last year is 34, now is 31

## Slide 6
GPS
Present and future GPS signal
  Block I (1978-1985): L1 (C/A), L1 and L2 (P-code)
  Block IIR-M (2005-2009): L2 (L2C), L1 and L2 (M-code), L5
  Block IIF (2010-2016): Civil code on L5
  Block III (2018-): L1C
Notes: BOC: Binary offset carrier modulation
Reduce error rate, more flexible, less code noise, improve the L1 Civil signal

## Slide 7
GPS
https://www.gpsworld.com/the-almanac/
GPS Almanac
SV Number: refers to space vehicle number.
PRN Number: refers to the satellite’s unique pseudorandom noise code.
Clock: Rb = rubidium; Cs = cesium.
Launched and Usable dates: are based on Universal Time.
Notes: BOC: Binary offset carrier modulation
The current active GPS constellation consists of 1 Block IIA, 11 Block IIRs, 7 Block IIR-Ms and 12 Block IIFs for a total of 31 satellites and is under FOC (Full Operational Capability).

## Slide 8
1982
3 Orbital planes
MEO
1996, 21 Satellites + 3 Spares (currently 24)
64.8 ° Inclination Angle
Altitude 19, 100km
8/17 sidereal day period
GLONASS
https://www.e-education.psu.edu/geog862/node/1872
Notes: Only 7 healthy satellites remained in 2001. After that, a program to rebuild and modernize GLONASS.
It is higher than GPS
https://en.wikipedia.org/wiki/GLONASS

## Slide 9
GLONASS
http://ftp.aiub.unibe.ch/BERN42/DOCU/DOCU42_2.pdf
GPS vs GLONASS Ground Track
GLONASS
GPS

## Slide 10
GLONASS
https://en.wikipedia.org/wiki/List_of_GLONASS_satellites
GLONASS satellite
Notes: Last year 24

## Slide 11
GLONASS
https://en.wikipedia.org/wiki/List_of_GLONASS_satellites
GLONASS future plan
Notes: 1993, 24 satellites

## Slide 12
GLONASS
https://www.e-education.psu.edu/geog862/node/1874
Present and future GLONASS signal
Notes: GLONASS has only one PRN code, starting for GLONASS-K, it will be more like GPS code.
BOC: Binary offset carrier modulation, more like GPS code
FDMA (Frequency Division Multiple Access); This approach is known as CDMA (Code Division Multiple Access)
The first is L1 (~1602 MHz), in which the separation between individual carriers is 0.5625 MHz; the range is between ~1598.0625 to ~1607.0625 MHz. The second is L2 (~1246 MHz), in which the separation between individual carriers is 0.4375 MHz; the range is between ~1242.9375 to ~1249.9375 MHz. The third is L3. This third civil signal on L3 is available on the K satellites and within a new frequency band (~1201 MHz) that includes 1201.743 to 1208.511 MHz and will overlap Galileo’s E5B signal.
The open signal L3OC is centered at 1202.025 MHz and uses BPSK(10) modulation for both data and pilot channels; the ranging code transmits at 10.23 million chips per second, modulated onto the carrier frequency using QPSK with in-phase data and quadrature pilot.

## Slide 13
GLONASS
https://www.gpsworld.com/the-almanac/
GLONASS Almanac
The Russian Federation designated the Kosmos Number.
Channel number k indicates L1 and L2 carrier frequencies: L1 = 1,602 + 0.5625 k (MHz); L2 = 1,246 + 0.4375 k (MHz).
All launch and usable dates are based on Moscow Time (Universal Time + 3 hours).
Notes: The Russian Federation designated the “Kosmos Number.”
Channel number “k” indicates L1 and L2 carrier frequencies: L1 = 1,602 + 0.5625 k (MHz); L2 = 1,246 + 0.4375 k (MHz).

## Slide 14
2005
3 Orbital planes
MEO
30 satellite (currently 24， as of December 2021)
56° Inclination Angle
Altitude 23, 222 km
10/17 sidereal day period
Galileo
https://www.e-education.psu.edu/geog862/node/1876
Notes: 1993, 24 satellites, inclination maybe changed
Two Galileo sent to wrong orbits

## Slide 15
Galileo
http://positimgnss.blogspot.com/2014/08/groundtrack-of-galileo-satellites.html
Galileo Ground Track
Notes: The figures shows the ground track of Galileo-101 (E11), one of the older Galileo satellites, and Galileo-201, one of the two new Galileo satellites, over a period of 24 hours for August 23, 2014. A couple of interesting features can be seen from the plot. Firstly the difference in inclination, 56 vs 49 degrees, is clearly visible as the maximum latitude of the Galileo-201 satellite is clearly smaller.

## Slide 16
Galileo
https://en.wikipedia.org/wiki/Galileo_(satellite_navigation)
Galileo satellite
https://www.e-education.psu.edu/geog862/node/1876

## Slide 17
Galileo
https://en.wikipedia.org/wiki/List_of_Galileo_satellites
Galileo future plan
Notes: 1993, 24 satellites

## Slide 18
Galileo
https://en.wikipedia.org/wiki/Galileo_(satellite_navigation)
Present and future Galileo signal
Notes: BOC: Binary offset carrier modulation, copy GPS system. L1 and L5
Full Operational Capability
Therefore, BPSK-modulated signals such as C/A GPS codes have most of their spectral energy concentrated around the carrier frequency, while BOC-modulated signals (used in Galileo system) have low energy around the carrier frequency and two main spectral lobes further away from the carrier (thus, the name of split-spectrum). https://en.wikipedia.org/wiki/Binary_offset_carrier_modulation

## Slide 19
Galileo
https://www.gpsworld.com/the-almanac/#galileo
Galileo Almanac
NORAD ID is assigned by USSPACECOM to all Earth orbit satellites in order of identification.
Notes: Satellites launched into wrong orbits.
Orbit perigree raised by about 3500 kilometers in November 2014.
Clock failures in 2017

## Slide 20
2000
7 Orbital planes (3 MEO+1GEO+3IGSO)
44 Satellites (27 MEO, 7 GEO, and 10 IGSO)
55° Inclination Angle
7/13 sidereal day period
Altitude 21, 500 km
Beidou
https://www.e-education.psu.edu/geog862/node/1879
Notes: Initiated 1994
inclined geosynchronous orbits (IGSO)
June, 2020
The IGS01, IGS02 and IGS03 satellite are at ~120°E. IGS04 and IGS05 are at ~95°E.
https://gssc.esa.int/navipedia/index.php/BeiDou_Space_Segment

## Slide 21
Beidou
https://www.researchgate.net/figure/Ground-tracks-of-Global-Positioning-System-GPS-satellites-Beidou-Satellite-Navigation_fig1_325124152
Beidou Ground Track
Notes: 1993, 24 satellites, sinusoid, symmetric

## Slide 22
Beidou
https://en.wikipedia.org/wiki/Global_Positioning_System
Beidou satellite
https://directory.eoportal.org/web/eoportal/satellite-missions/content/-/article/cnss
Notes: 1993, 24 satellites

## Slide 23
Beidou
https://www.e-education.psu.edu/geog862/node/1879
Beidou signal
Notes: BOC: Binary offset carrier modulation
BeiDou satellites currently transmit signals in three bands; B1 (1561.098 MHz), B1-2 (1589.742 MHz), B2 (1207.14 MHz) and B3 (1268.52). The modulation scheme is quadraphase shift key (QPSK)

## Slide 24
Beidou
https://www.gpsworld.com/the-almanac/
Beidou Almanac
Notes: BOC: Binary offset carrier modulation
1OV test satellite, but in operation
GEO, formerly at 84° E, shifted to 110.5° E between about Nov. 7 and Nov. 23, 2012.
Satellite is not currently transmitting standard signals.

## Slide 25
2010
4 Orbital planes (3 IGSO and 1 GEO)
GEO
7 Satellites (currently 4)
40° Inclination Angle
Altitude 32, 000 – 40,000 km
1 sidereal day period
QZSS (Quasi-Zenith Satellite System)
https://www.e-education.psu.edu/geog862/node/1880
Notes: 10 years design life, Quasi-Zenith Satellite System (QZSS), in the sbas page

## Slide 26
QZSS
https://www.e-education.psu.edu/geog862/node/1880
Ground Track

## Slide 27
https://en.wikipedia.org/wiki/Quasi-Zenith_Satellite_System
QZSS satellite
QZSS
Notes: 1993, 24 satellites

## Slide 28
https://qzss.go.jp/en/overview/services/sv01_what.html
QZSS future plan
QZSS
Notes: 1993, 24 satellites

## Slide 29
https://gssc.esa.int/navipedia/index.php/QZSS
Present and future QZSS signal
QZSS
Notes: The system transmits 6 signals, L1-C/A, L1C. L2C, L5 are similar with GPS siganal
Navigation and Timing Service

## Slide 30
QZSS
https://www.gpsworld.com/the-almanac/#SBAS
QZSS Almanac
Notes: N. On June 2, 2018, QZS-3 suffered a signal amplifier switch failure. During trouble shooting, all test signals from QZS-2, QZS-3 and QZS-4 have been temporally halted since June 4, 2018

## Slide 31
2013
3 Orbital planes (1 IGSO and 2 GEO)
GEO
2018, 7 Satellites
29° Inclination Angle
Altitude 35,700 km
1 sidereal day period
IRNSS (Indian Regional Navigation Satellite System)
https://spaceflight101.com/spacecraft/irnss/
Notes: 2006 planed, Indian Regional Navigation Satellite System, 3 GEO satellite and 4 GSO satellite, 9.5 -11 years , 2 spare are also planed
Altitude 35,700 km (GEO)

## Slide 32
IRNSS
https://directory.eoportal.org/web/eoportal/satellite-missions/content/-/article/irnss
Ground Track

## Slide 33
https://en.wikipedia.org/wiki/Indian_Regional_Navigation_Satellite_System
IRNSS future plan
IRNSS
Notes: 1993, 24 satellites

## Slide 34
https://www.gpsworld.com/the-almanac/
IRNSS satellite
IRNSS
IRNSS Almanac
Notes: A. Decommissioned.

## Slide 35
Present and future IRNSS signal
  L5 (1176.45 MHz)
  S band (2492.028 MHz)
  Standard Positioning Service and Precision Service
IRNSS
Notes: Binary offset carrier modulation
NavIC signals will consist of a Standard Positioning Service and a Precision Service. Both will be carried on L5 (1176.45 MHz) and S band (2492.028 MHz).[54] The SPS signal will be modulated by a 1 MHz BPSK signal.

## Slide 36
Why GNSS?
Stanford University
Availability for Accuracy
Notes: BOC: Binary offset carrier modulation

## Slide 37
Why GNSS?
Stanford University
Availability for Robustness
Notes: BOC: Binary offset carrier modulation

## Slide 38
Why GNSS?
Stanford University
Jamming immunity
Notes: BOC: Binary offset carrier modulation

## Slide 39
GNSS Application
Availability for Accuracy
  Consumer
  Ground Mapping
  Transportation
  GIS
  Machine Control
  Port Automation
  Precision Agriculture
  Timing
  Construction
  Marine
  Unmanned Vehicles
  Surveying
  Defense
  Aerial Photogrammetry
Notes: BOC: Binary offset carrier modulation

## Slide 40
https://www.engineering.com/BIM/ArticleID/18792/The-Rest-of-the-Industrialized-World-Has-High-Speed-Rail-Why-Cant-the-US.aspx
GNSS Application
Notes: BOC: Binary offset carrier modulation

## Slide 41
GNSS Application
https://www.sohu.com/a/417142570_188923?spm=smpc.tag-page.fd-news.2.1599713094475OGM13K4
https://www.intechopen.com/books/new-approach-of-indoor-and-outdoor-localization-systems/gnss-in-precision-agricultural-operations

## Slide 42
Project Introduction
Notes: BOC: Binary offset carrier modulation

## Slide 43
Urban Tree: Environment Justice
Fang et al., 2022 under review
Notes: BOC: Binary offset carrier modulation

## Slide 44
Urban Tree: Environment Justice
Fang et al., 2022 under review
Notes: BOC: Binary offset carrier modulation

## Slide 45
Urban Tree: Environment Justice
Fang et al., 2022 under review
Notes: BOC: Binary offset carrier modulation

## Slide 46
Urban Tree: Environment Justice
City of Conway
Notes: BOC: Binary offset carrier modulation

## Slide 47
Urban Tree: Environment Justice
City of Conway
Notes: BOC: Binary offset carrier modulation

## Slide 48
Conway Tree Board
Annual Arbor Day Festival on November 5th from 11 am-1 pm in Laurel Park
With our Adopt A Tree activity where kids will be invited to pick a tree, measure, and make note of the tree attributes to earn their tree adoption certificate and tree journal. This would be a good activity that allows us to share the data we've collected while teaching children to do the same.
We can host our own table/ exhibit to share our own work to help educate attendees about the benefits of public trees in Conway.
Notes: BOC: Binary offset carrier modulation

## Slide 49
Thank you!