## Slide 1: WEEK 07 drone lecture
Instructor: Yanan Wu
fALL 2025

## Slide 2: 7.1 drone

## Slide 3
All drones weight more than .55 pounds must be registered
  The only real, valid drone registration site is faadronezone.faa.gov
  Any other site purporting to ‘help’ or ‘streamlining’ your registration is fake
Safety and Regulation

## Slide 4
All drones weight more than .55 pounds must be registered
  The only real, valid drone registration site is faadronezone.faa.gov
  Any other site purporting to ‘help’ or ‘streamlining’ your registration is fake
Safety and Regulation

## Slide 5
You must have a drone license
  Have passed the Part 107 aeronautical knowledge test (Airspace, radio communication, remote operation, weather theory, sectional charts, and so on. 60 Questions, 70% to pass)
Safety and Regulation

## Slide 6
You must have a drone license
  Are at least 16 years of age
  Have been vetted by the Transportation Security Administration
  If you are flying as a hobbyist or as part of a public (government) team, Part 107 does not appl
Safety and Regulation

## Slide 7
You may need authorization near airports
  Controlled airspace: B, C, D, E
  Uncontrolled airspace: G
  B C, D and E surface area: Authorization required
Safety and Regulation

## Slide 8
You may need authorization near airports
  Authorization are applied through FAA not less than 90 days before the planned operations
Safety and Regulation

## Slide 9
No flying above 400 ft AGL
  With some exceptions
  If you are already higher than 400 feet (e.g., on top of building), you must remain within 400 feet of the structure in any direction
Safety and Regulation

## Slide 10
No flying beyond visual line of sight (VLOS)
  You must be able to see and assess risk at all times during the flight
  If you can’t see the sky around the drone, or the ground below the drone, you’re not within visual line of sight
Safety and Regulation
Visual line of sight (107.31) is defined by being able to:
1.Know the unmanned aircraft’s location;
2.Determine the unmanned aircraft’s attitude, altitude and direction of flight;
3.Observe the airspace for other air traffic or hazards
4.Determine that the unmanned aircraft does not endanger the life or property of another

## Slide 11
No flying over people
  Unless they are part of team
  The drone must not put anyone at risk if the drone was to fall
Safety and Regulation

## Slide 12
The person operating the drone controls must hold a remote pilot certificate, or be under the direct supervision of, and within close proximity to, someone who does.
A remote pilot must have his/her pilot certificate on his/her person or within easy access while acting as Pilot in Command. A remote pilot must also be able to show 24-calendar month recurrency.
Safety and Regulation

## Slide 13
If you change your permanent address you must notify the FAA Airman Certification branch of the new address within 30 days
You may choose to use a Visual Observer (VO) to supplement situational awareness
You must report to the FAA within 10 calendar days of any operation that results in serious injury, loss of consciousness, or property damage of $500 or more
Safety and Regulation

## Slide 14
You must give way to any manned aircraft. Do not fly under unmanned balloons
You must only fly one drone at a time
You may not fly faster than 100 mph
You may not operate the drone from a moving aircraft, but you may operate the drone from a moving vehicle if you are flying over a sparsely populated area
Safety and Regulation

## Slide 15
You may not fly recklessly or in any way that endangers the life or property of another person
You may not fly if you are tired, mentally or physically impaired
You may not fly if you have consumed alcohol within the prior 8 hours, or with a blood alcohol content of 0.04% or greater
Safety and Regulation

## Slide 16
You may fly during civil twilight or night with appropriate anti-collision lighting, visible for at least 3 statute miles
Civil twilight is defined as 30 minutes before official sunrise and 30 minutes after official sunset. Night is defined as the period between the end of evening civil twilight and beginning of morning civil twilight
Night flight may need waiver and has additional requirement of passing a Part 107 after 04/05/2021
Safety and Regulation

## Slide 17
You must have 3 statute miles of visibility
You must remain at least 500 feet below and 2,000 feet horizontally from clouds
You may not fly anywhere that may interfere with the operation of an airport. This includes, but is not limited to, approach corridors, traffic patterns, taxiways, runways, and helipads
The drone plus additional cargo may not weigh 55 pounds or more
Safety and Regulation

## Slide 18
DJI Phantom 2
  Is basic and somewhat antiquated
  Cost < $300 (if you can find them)
  Have smart battery
  Have approximately 20 minutes of flight time
  DJI products are prohibited for most federal agencies
Drone

## Slide 19
DJI Phantom 4 Pro
  Weight 1,380 g
  Cost $1,599
  Have smart battery
  Have approximately 28 minutes of flight time
  Max transmission distance: 2.2 mi to 3.1 mi
  Satellite positioning systems: GPS/GLONASS
Drone

## Slide 20
Conduct a preflight inspection of the drone to make sure it is in a condition for safe operation
Check for all Notices To Airmen (NOTAMs) to determine if there are any applicable airspace restrictions
Conduct an assessment of the operating environment
Obtain local weather information
Obtain local airspace information and restrictions
Locate and access persons and property in the area, as well as all other potential ground hazards
Ensure that all control links between the control system and the drone are working properly
Ensure there is sufficient power to continue flight operations to a normal landing
Drone preflight checking
Notes: A NOTAM is a notice containing information essential to personnel concerned with flight operations but not known far enough in advance to be publicized by other means. It states the abnormal status of a component of the National Airspace System (NAS) – not the normal status

## Slide 21
Drone preflight checking
Download and Install the App
Search three locations:
  Your current location
  Bill and Hillary Clinton National Airport
  Downtown Grill, Conway
https://portal.airspacelink.com/
https://www.faa.gov/uas/getting_started/b4ufly
Notes: A NOTAM is a notice containing information essential to personnel concerned with flight operations but not known far enough in advance to be publicized by other means. It states the abnormal status of a component of the National Airspace System (NAS) – not the normal status

## Slide 22
Drone preflight checking
Download and Install the App
Create an account
GEO Zones
DJI GO 4
Notes: A NOTAM is a notice containing information essential to personnel concerned with flight operations but not known far enough in advance to be publicized by other means. It states the abnormal status of a component of the National Airspace System (NAS) – not the normal status

## Slide 23
Mission Plan
Better data
  Same altitude, fly speed, and so on
  Replicate missions
  This is helpful with time series analyses!
  It’s automated
  Save time
Drone Camp

## Slide 24
Mission Plan
Input into a mission plan
  Project goals
  Size of study area
  Required GSD (Ground Sample Distance)
  Ground cover type
  Sensor
  Platform
  Spatial accuracy needs
Drone Camp

## Slide 25
Mission Plan
Goals and Aspirations
  sensor type
  preferred GSD
  size of study area
  preferred aircraft
  repeatability
Drone Camp

## Slide 26
Mission Plan
Logistic and Constraints
  airspace & local permissions
  site access & launch points
  time available for field work
  flight time, # batteries
  wind & weather
  sun & shadows
  data processing resources
Drone Camp

## Slide 27
Mission PlanW
Rules of Thumb
  Visibility
    Fly at least double the height of trees
  Large areas
    Plan your mission so you are flying back toward yourself
    Consecutive flights need begin where the last one ended
  Challenging terrain
    Launch from the highest altitude possible
  Challenging surface cover
    Photogrammetry of whipping grass in the wind is most difficult with low altitude flights
Drone Camp

## Slide 28
Mission Plan
Overlap
  Minimum
    75% frontal overlap
    60% side overlap
  BUT this depends
    Higher overlap is needed for thermal imagery and high relief terrain
Drone Camp

## Slide 29
Mission Plan
Overlap
  Agriculture and dense vegetation
    85% frontal overlap
    80% side overlap
  Aim for 5-10 cm/pixel GSD
Drone Camp

## Slide 30
Mission Plan
Select a launch point
  Launch high for safety & better GPS reception
  Flat is good
  Level is even better
  Away from obstacles
  Sun at your back
  Downwind from AOI (area of interest)
  Minimize time between flights
  Use a landing pad in dusty environments
Drone Camp

## Slide 31
Mission Plan
Ground Control Points
  Need precise geo-registration for overlays
  Need to mosaic multiple flights over complex topography
Drone Camp

## Slide 32
Mission Plan
Mission Planning Apps
Drone Camp
Pix4D Capture
DroneDeploy
Precision Flight
DJI Pilot

## Slide 33
Mission Plan
Mission Planning Apps
Drone Camp
Map Pilot
Litchi
DJI Ground Station Pro
Drone Harmony
QGroundStation

## Slide 34
Mission Plan
Outputs
Drone Camp
Orthomosaic
DSM
Veg Indices
Textured Mesh
Point Cloud

## Slide 35
Application of Drone
Power inspection

## Slide 36
Thank you!